MIDLANDS LUBRICANTS LTD.

Technical Data Sheet

Pro Cut 22 FAM

Chlorine and Sulphur free neat cutting oil

Midlands Lubricants Pro Cut 22 FAM is a chlorine and sulphur free neat cutting oil developed for use on ferrous and non-ferrous materials across a wide range of machinery. Typical applications include general machining on bar autos and automatic machines, drilling, milling and turning.

Midlands Lubricants Pro Cut 22 FAM combines specially selected high performance additives - lubricity, antimist and anti- oxidant making it suitable for use on all types of steel and non-ferrous materials.

| Pro Cut 22 FAM is a low viscosity product and is an excellent choice for use on CNC sliding head lathes where manufacturers require a flexible option for high performance machining with good lubrication minimum product drag out. The products low viscosity ensures rapid penetration to the cutting tool / work piece zone where a viscosity grade of ISO 15 – 22 is required. Application & Benefits  Drilling and Boring  Turning  Milling  Medium duty machining  Ferrous and Non Ferrous materials  Dual purpose oil where specified  Excellent performance characteristics  Contains NO Sulphur or Chlorine  Contains Anti-mist additive  Anti oxidant formulation to maximise oil life  Formulated on high quality mineral oil  Light Colour  Excellent finish properties  Can be recycled using our recovery service Directions for use |
| --- |
| Shelf life 3 years from date of manufacture |
| Designed to be used as supplied and is safe to use on most metals. |
| Store sealed in a cool dry place between 5°C and 30°C material should always be stored indoors and protected from extremes of temperature. |
| For guidance on handling and disposal please refer to the Material Safety Data Sheet |
| Pro Cut 22 FAM |
| Characteristics | Typical Data | Characteristics | Typical Data |
| Appearance | Amber | Chlorine | No |
| Viscosity @40oC | 22 cst | Ester | Yes |
| Specific Gravity | 0.875 | Sulphur | No |